## Slide 1: Monte carlo Simulation of a Medical Linear Accelerator
Seenia Francis
P190029CS
CSED
Guide :
Dr. Jayaraj P B
Dr. Pournami P N
Date : 26/07/2019

## Slide 2: Introduction
Cancer is one of the major death reason in the world.
Cancer treatment will be one of the greatest health challenges of the 21 century.
Radiotherapy is one of the most important and common treatment of cancer.
  Is a local treatment of cancer with ionizing radiation
The equipment more often used for radiotherapy is a Linear Accelerator
  Which produce X-ray beams in the range from 5 to 30 MeV
The accuracy in the Radiotherapy planning is very important in the evaluation of dose.
Among many algorithms, methods based on Monte Carlo have proven to be very promising in terms of accuracy.

## Slide 3: Ionizing Radiation
Energy emitted from a source is generally referred to as radiation.
Ionizing radiation is radiation with enough energy so that during an interaction with an atom, it can remove tightly bound electrons from the orbit of an atom, causing the atom to become charged or ionized.
Ionizing radiation is any type of particle or electromagnetic wave that carries enough energy to ionize or remove electrons from an atom.
Two type of electromagnetic waves can ionize atom
  X-rays and gamma rays
Why ionization radiation is dangerous?
  When atoms in living things become ironized
    The cell dies
    The cell repair itself
    The cell mutates incorrectly and can become cancerous
Radiation is effective as a cancer treatment because it can kill cancer cells. But when used it must be pinpointed very carefully without disturbing nearby cells.

## Slide 4: Dosimetric Evaluation
  The simulation of the production of the radiation beam from Linac (ELECTA) and the generation of phase space. (Set of Information about the particle state- energy, position, direction)
  Patient simulation and evaluation of various parameters affecting dose distribution in the body
Conventionally, the object representation is obtained from the computed tomography images
The dosimetric evaluation procedure in radiotherapy is normally divided into two stages
Figure 1: Representation of the MC simulation model commonly used for applications in radiotherapy divided into two stages.

## Slide 5: Monte Carlo simulation
It is a technique used to understand the impact of risk and uncertainity.
The MC methods perform numerical simulation of problems using essentially a sequence of random numbers.
These statistical methods may be used to simulate the behavior of physical systems, mathematical, biological, etc. which can be described by random sampling of probability density functions (PDFs).

## Slide 6: Simulation of Radiation Transport
In the simulation of radiation transport using MC methods,
  The history of a particle is defined as a sequence of tracks where each track ends with an interaction event where the particle can change its direction, lose energy and occasionally produce secondary particles.
  The history ends when it leaves the region of interest or when its energy is lower than the predefined cutoff energy.
  In the latter case, the remaining energy is deposited at the point where the transport of the particle was stopped.
The Geant4 is one of the main MC codes used in medical physics, such as radiotherapy with heavy particles and image-guided radiation therapy

## Slide 7: Simulation for Parallel computing
MC codes frequently allow evaluate the radiation effects with great accuracy.
However, the accuracy of the simulation is a direct function of the number of histories and, consequently, of the simulation time.
A long simulation time is inappropriate for some applications that would benefit much from its accuracy, but require a quick response.
Parallel processing have been widely exploited as a suitable technique to reduce the simulation time.
Parallel computing is a computing way which various processes are executed simultaneously using hardware resources to solve a particular problem .
The G4MPI is a native interface of the Geant4 for parallel computing that uses the libraries MPI (Message-Passing Interface) and implements the parallelism for simulation of separated histories on remote processors.
Using this interface, user applications can be parallelized with different MPI libraries such as LAM/MPI, MPICH2, OpenMPI, etc.

## Slide 8: Simulation of Linear Accelerator
To simulate the production of the photon beam of a Linac, it is necessary to define in detail the components of the head which have influence in the output beam.
Commonly, these components are
  Ttarget,
  Primary collimator,
  Flattening filter,
  Ionization chamber,
  Mirror and
  Secondary collimator (Fig. 2a).
The target, the primary collimator and flattening filter are the components of the Linac that have the most influence on the shape of the photon spectrum.

## Slide 9: Components of a Linac head
In a Linac electrons gain energy by interacting with an electromagnetic field of synchronized radio frequency.
The accelerator structure consists of a long cylindrical tube having a series of solenoids which creates an electromagnetic field.
When the electron beam leaves the accelerator tube, it is bent by magnetic fields, so it forms a collimated beam approximately 2 to 3 mm in diameter and hit the target normally .
Thus, the primary electron beam can be determined by two main characteristics:
  The size (diameter) of the focal point and the energy average.

## Slide 10: Linear accelerator ....
Target
  A tungsten or a laminate of copper-tungsten thin enough to completely stop the primary electrons.
  The energy lost by electron is converted into X-ray photons whose main emission is directed forward.
Flattening filter
  To compensate for the lack of scattering at the edge of the field, it is used a flattening filter that projects deliberately a beam profile which increases toward the edges(Fig. 2c).
  The filters have a conical shape and are generally circularly symmetric.
  The material should be made of medium atomic number, such as steel and copper .

## Slide 11: Linear accelerator ....
Collimators
  It is device which narrows a beam of particles or wave. To narrow can mean either to cause the direction of motion to become more aligned in a specific direction (parallel rays) or to cause the spatial cross section of the beam to become smaller.
  The head of a Linac has two collimators to ensure that only the treatment area is irradiated.
  The primary collimator is fixed and the secondary one is adjustable.
  The material is usually tungsten.
  The primary collimator field defines the maximum beam of X-rays, typically 40 × 40 cm to 100 cm from the source.
  The secondary collimators consist of two pairs of jaws, one above the other.
  The jaws are labeled X1, X2 and Y1, Y2. Its edges often define arcs such that their inner faces are approximately tangential to the beam of radiation, thereby reducing the penumbra.
  In order to enable the location of the X-ray beam, a light beam is generated to match the limits of the useful radiation beam. This is achieved by means of reflection of a high intensity light source located outside of the radiation field.

## Slide 12: Linear accelerator ....
Ionization chamber
  A gas filled radiation detectors, and is used for the detection and measurement of certain type of ionizing radiation. Detectors which collect all the charges created by direct ionization within the gas through the application of an electric field
A detector of ionization chamber type is used to obtain measurements of the amount of radiation provided by accelerator and also to control the uniformity and symmetry of the beam.
The ionization chambers are of transmission type of parallel plate with large diameter for monitoring the total field.
In some Linacs, the signal of the ionization chamber is affected by the position of the secondary collimator.
Backscattered particles of collimators can generate additional charges in the chamber.

## Slide 13: Linear accelerator ....
To assess the dose distribution in a particular geometry, it is necessary that the state of particles in the incident beam is accurately known, i.e., energies, directions and positions of the photons, electrons, and positrons.
This data set is called phase space.
The obtaining of the phase space in MC simulations of Linac is accomplished by defining a sensitive volume that stores the information of the particles that pass through it.
Generally, this volume is a thin circular cylinder located just above the secondary collimator. In this case the phase space becomes a virtual Linac and can be used in different simulations.
However, one should pay attention to the amount of particles stored in the phase space so will be sufficient sample to obtain the expected accuracy.

## Slide 14
Here ends the first part of the dosimetric simulation that is the simulation of linear accelerator and creation of phase space.
Next is the Patient simulation and evaluation of dose distribution in the body

## Slide 15: Thank you